## Slide 1
Dayananda Sagar College of Engineering
(Shavige Malleshwara Hills, Kumaraswamy Layout, Bengaluru – 560 078)
Department of Electronics and Communication Engineering
NAME
Vishvendra Singh
Tanvi Vijay
Saurabh Singh
Sameer Gautam
USN
1DS18EC156
1DS18EC153
1DS18EC144
1DS18EC143
Emerging Technology Mini-Project
PHYSICAL LAYER WIRED AND WIRELESS SECURITY

## Slide 2: INDEX
Overview
Physical Security in Wired Networks
Physical Security in Wireless Networks

## Slide 3
Networks are made up of devices and communication links.
Devices and links can be physically threatened.
  Vandalism, lightning, fire, excessive pull force, corrosion, wildlife, wear-down, wiretapping, crosstalk, jamming.
We need to make networks mechanically resilient and trustworthy.
INTRODUCTION

## Slide 4
3

## Slide 5: How can two computers communicate?
Encode information into physical “signals”
Transmit those signals over a transmission medium

## Slide 6
Metal (e.g., copper): wired
EM/RF (e.g., IEEE 802.11): wireless
Light (e.g., optical fiber)
TYPES OF MEDIA

## Slide 7: Noise, Jamming, and Information Leakage
When you move a conductor through a magnetic field, electric current is induced (electromagnetic induction)
  EMI is produced from other wires or devices
  Induces current fluctuations in conductor
  Problem: crosstalk, conducting noise to equipment, etc
16
PHYSICAL SECURITY IN WIRED NETWORKS

## Slide 8
Conductive Taps
  Form conductive connection with cable
Inductive Taps
  Passively reads signal from EM induction
  No need for any direct physical connection
  Harder to detect
  Harder to do with non- electric conductors (e.g., fiber optics)
24
PHYSICAL TAPPING

## Slide 9
TAPPING CABLE: COUNTERMEASURES
Physical inspection
Physical protection
  E.g., encase cable in pressurized gas
Use faster bitrate
Monitor electrical properties of cable
  TDR: sort of like a hard-wired radar
  Power monitoring, spectrum analysis
25

## Slide 10: CASE STUDY: SUBMARINE CABLE (IVY BELLS)
1970: U.S. learned of USSR undersea cable
  Connected Soviet naval base to fleet headquarters
Joint US Navy, NSA, CIA operation to tap cable in 1971
Saturation divers installed a 3-ft long tapping device
  Coil-based design, wrapped around cable to register signals by induction
  Signals recorded on tapes that were collected at regular intervals
  Communication on cable was unencrypted
  Recording tapes collected by divers monthly
26

## Slide 11: CASE STUDY: SUBMARINE CABLE (IVY BELLS)
1972: Bell Labs develops next-gen tapping device
  20 feet long, 6 tons, nuclear power source
  Enabled
No detection for over a decade
  Compromise to Soviets by Robert Pelton, former employee of NSA
Cable-tapping operations continue
  Tapping expanded into Pacific ocean (1980) and Mediterranean (1985)
  USS Parche refitted to accommodate tapping equipment, presidential commendations every year from 1994-97
  Continues in operation to today, but targets since 1990 remain classified
27

## Slide 12
Rodents (squirrels, rats, mice, gophers)
  Chew on cables to grind foreteeth to maintain proper length
Insects (cicadas, ants, roaches, moths)
  Mistake cable for plants, burrow into it for egg laying/larvae
  Ants invade closures and chew cable and fiber
Birds (crows, woodpeckers)
  Mistake cable for twigs, used to build nests
Underground cables affected mainly by rats/termites, aerial cables by rodents/moths, drop cables by crows ,closures by ants
PROTECTION AGAINST WILDLIFE

## Slide 13: COUNTERMEASURES AGAINST WILDLIFE
Use High Strength Sheath cable
  PVC wrapping stainless steel sheath
  Performance studies on cable (gnathodynameter)
Cable wrap
  Squirrel-proof covers: stainless steel mesh surrounded by PVC sheet
Fill in gaps and holes
  Silicone adhesive
Use bad-tasting cord
  PVC infused with irritants
  Capsaicin: ingredient in pepper spray, irritant
  Denatonium benzoate: most known bitter compound
36

## Slide 14
Physical attacks: destroy sensors physically
Physical attacks are inevitable in sensor networks
  Sensor network applications that operate in hostile environments
    Volcanic monitoring
    Battlefield applications
  Small form factor of sensors
  Unattended and distributed nature of deployment
Different from other types of electronic attacks
  Can be fatal to sensor networks
  Simple to launch
Defending against physical attacks
  Tampering-resistant packaging helps, but not enough
  We propose a sacrificial node based defense approach to search-based physical attacks
PHYSICAL ATTACKS IN WSNS: WHAT & WHY?
Notes: Physical attacks can permanently destroy the sensors, which are different from electronic attacks such as jamming attacks, which tries to interfere the radio channels and interrupt the sensor networks’ operation.
Emphasize that physical attacks are simple to lunch.

## Slide 15
Two phases
  Targeting phase
  Destruction phase
Two broad types of physical attacks:
  Blind physical attacks
  Search-based physical attacks
PHYSICAL ATTACKS IN WSNS – A GENERAL DESCRIPTION

## Slide 16
BLIND PHYSICAL ATTACKS IN WSNS
Notes: Due to the brute-force destruction methods and blindly selecting attack areas

## Slide 17
Sensor network signals
  Passive signal and active signal
Attacker capacities
  Signal detection
  Attacker movement
  Attacker memory
Attack Model
  Attacker objective
  Attack procedure and scheduling
MODELING SEARCH-BASED PHYSICAL ATTACKS IN WSNS
Notes: Passive signals include heat, vibration, magnetic signals which are parts of the constant physical characteristics of the sensors. Active signals on the other hand include communication
messages, beacons, query messages etc., that are part of normal communications between sensors in the network.
Signal strength, active, passive signal detection range, active signal frequency
cluster-head: large active signal detection range, cluster-head rotation frequency
The cluster-head rotation is used to balance the power consumption and reduce the damage due to the destruction of the cluster-head
Isolation/detection accuracy
Attacker moving and destruction speed

## Slide 18
di: Estimated distance
θ: Isolation accuracy
  Direction/Angle of arrival
πri2: Isolation/sweeping area
  ri =di * θ
Attacker’s detection capacity is stronger than that of sensors
SIGNAL DETECTION

## Slide 19
f : Active signal frequency
Rnoti: message transmission range
Ra: The maximum distance the attacker is detected by active sensors
Rs: Sensing range
Rps: Max. distance for passive signal detection
Ras: Max. distance for active signal detection
v: Attacker moving speed
M: Attacker memory size
NETWORK PARAMETERS AND ATTACKER CAPACITIES

## Slide 20
AC: Accumulative Coverage
EL: Effective Lifetime, the time period before the coverage falls below a threshold α
Objective: Minimize AC
ATTACKER OBJECTIVE AND ATTACK PROCEDURE
Notes: AC measures both coverage and lifetime of sensor networks.
During the scheduling of attack activities, the attacker needs to choose between normal sensors and the cluster-head if the time cost to destroy them is same
Need more time to reach cluster-heads and the corresponding sweeping areas are larger.

## Slide 21: DISCUSSIONS ON SEARCH-BASED PHYSICAL ATTACKS IN WSNS
Differentiate sensors detected by active/passive signals
  Sensors detected by passive signals are given preference
Scheduling the movement when there are multiple detected sensors
  Choose sensors detected by passive signals first
  Choose the one that is closest to the attacker
  Optimal scheduling?
    Due the dynamics of the attack process, it is hard to get the optimal path in advance

## Slide 22: DEFENDING AGAINST SEARCH-BASED PHYSICAL ATTACKS IN WSNS
Assumptions
  Sensors can detect the attacker or
  Destroyed sensors can be detected by other sensors
  Attacker’s detection capacity is stronger than sensors, but not unlimited
A simple defense approach
Our sacrificial node based defense approach

## Slide 23: A SIMPLE DEFENSE APPROACH
: Attacker
: Sensor
Rnoti
s1
s3
s2
s4
s7
s6
s5
Rnoti
Rnoti

## Slide 24: OUR DEFENSE APPROACH
Adopting Sacrificial Nodes (sensors) to improve monitoring of the attacker and to increase the protection areas
  A sacrificial node is a sensor that keeps active in proximity of the attacker in order to protect other sensors at the risk of itself being detected and destroyed
  Attack Notifications from victim sensors
  States Switching of receiver sensors of Attack Notifications to reduce the number of detected sensors

## Slide 25: DEFENSE PROTOCOL
1: receive AN,
not be sacrificial node
2: receive AN,
be sacrificial node
3: not receive AN,
receive SN
4: T1 expires
5: T2 or T3 expires
6: destroyed by attacker
Sending
(nonsacrificial
node)
Sensing
Sending
(sacrificial node)
Destroyed
Sleeping
1
1
1
5
4
2
2
6
6
6
6
2
3
3
3

## Slide 26: AN ILLUSTRATION OF OUR DEFENSE APPROACH
: Attacker
: Sensor
Rnoti
s1
s3
s2
s4
s7
s6
s5
Rnoti
Rnoti

## Slide 27: DISCUSSIONS ON OUR DEFENSE PROTOCOL
Trade short term local coverage for long term global coverage
  Sacrificial nodes compensate the weakness of sensors in attack detection
  Our defense is fully distributed
Sacrificial node selection
  Who should be sacrificial nodes?
State switching - timers
  When to switch to sensing/sleeping state to prevent detection?
  When to switch back to sensing/sending state to provide coverage?

## Slide 28: SACRIFICIAL NODE SELECTION
Principle
  The more the potential nodes protected can be, higher is the chance to be sacrificial node
Solution
  Utility function u(i) is computed by each sensor based on local information
  Sensor i decides to be sacrificial node if u(i) ≥ Uth
  Uth = β * Uref (0<β<1); Uref = N * π * R2noti / S

## Slide 29: UTILITY FUNCTION U(I)
What is the basic idea of u(i)?
The more nodes being protected, the larger u(i) is
Overlap is discounted
Distance matters
Theorem 1: The utility function u(i) is optimal in terms of minimizing the expected mean square error between u(i) and uopt(i)

## Slide 30: STATE SWITCHING
D(i): Random delay for SN message
T(i): timers for states switching

## Slide 31: PERFORMANCE EVALUATION
Network parameters:
  S: 500 * 500 m2
  N: 2000
  α: 0.5
  f: 1 / 60 second
  Rnoti: 20 m
  Ra: 0.1 m
  Rs: 10 m
Attack parameters:
  Rps: 5 m
  Ras: 20 m
  v: 1 m/second
  M: 2000
Protocol parameters:
  β: 0.7
  Δt: 0.01 second
  T: 20 seconds

## Slide 32: DEFENSE EFFECTIVENESS UNDER DIFFERENT NETWORK PARAMETERS

## Slide 33: DEFENSE EFFECTIVENESS UNDER DIFFERENT ATTACKER PARAMETERS

## Slide 34: SUMMARY
Physical Security in Wired Networks
  Tapping attacks
  Case studies
Physical Security in Wireless Networks
  Physical attacks are patent and potent threats to sensor networks
  A Sacrificial Node-assisted approach to defend against physical attacks
Cryptography